## Slide 1: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return 1; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 2: Non-Leaf Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call
lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 3: Non-Leaf Procedure Example
MIPS code: (example of fact (2))
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # $a0 = 2 slti $t0, $a0, 1 # 2 > 1, $t0 = 0 beq $t0, $zero, L1 # $t0==0, go to L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # $a0 = 2 – 1 = 1 jal fact # recursive call fact(1)
lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return
fact(2)

## Slide 4: Non-Leaf Procedure Example
MIPS code: (example of fact (2))
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # $a0 = 1 slti $t0, $a0, 1 # 1 < 1, false, $t0 = 0 beq $t0, $zero, L1 # $t0==0, go to L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # $a0 = 1 – 1 = 0 jal fact # recursive call fact(0)
lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return
fact(1)

## Slide 5: Non-Leaf Procedure Example
MIPS code: (example of fact (2))
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # $a0 = 0 slti $t0, $a0, 1 # 0 < 1, $t0 = 1 beq $t0, $zero, L1 # $t0!=0, go on addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return to fact(1) L1: addi $a0, $a0, -1 # $a0 = 1 – 1 = 0 jal fact # recursive call fact(0)
lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return
fact(0)

## Slide 6: Non-Leaf Procedure Example
MIPS code: (example of fact (2))
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # $a0 = 1 slti $t0, $a0, 1 # 1 < 1, false, $t0 = 0 beq $t0, $zero, L1 # $t0==0, go to L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # $a0 = 1 – 1 = 0 jal fact # recursive call fact(0)
lw $a0, 0($sp) # restore original n (1) lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # $v0 = 1 x 1 = 1 jr $ra # and return to fact(2)
fact(1)
XYZ

## Slide 7: Non-Leaf Procedure Example
MIPS code: (example of fact (2))
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # $a0 = 2 slti $t0, $a0, 1 # 2 > 1, $t0 = 0 beq $t0, $zero, L1 # $t0==0, go to L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # $a0 = 2 – 1 = 1 jal fact # recursive call fact(1)
lw $a0, 0($sp) # restore original n(2) lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # $v0 = 2 x 1 = 2 jr $ra # and return
fact(2)
fact(2) = 2
XYZ

## Slide 8: Non-Leaf Procedure Example Local Data on the Stack
High address
$sp
High address
High address
$sp
Before procedure
After procedure
In procedure
XYZ
0
$ra of fact(2)
$ra of fact(1)
$sp
$ra of main
2
XYZ
1